Provision of Environmental incentives – Tonnage Tax System

1. Background

Sections 9(1) and 13(1) of the Merchant Shipping (Fees and Taxing Provisions) Laws of 2010-2020 (Law No. 44 (I) of 2010 as amended by Law 39(I)/2020) provide for a reduction/discount of up to 30% on the Annual Tonnage Tax paid by owners of Cyprus ships and Community ships that use mechanisms-equipment for the environmental preservation of the marine environment and the reduction of the effects of climate change.

2. Environmental Incentives

2.1 Incentive 1: Energy Efficiency Existing Ship Index (EEXI)

The Environmental Incentive related to the Energy Efficiency Existing Ship Index (EEXI) applies to ships that are subject to the provisions of Regulations 19, 23 and 25 of the amended MARPOL Convention/ANNEX VI.

Ships which achieve a reduction of the Attained Energy Efficiency Existing Ship Index (Attained EEXI) in relation to the Required Energy Efficiency Existing Ship Index (Required EEXI), greater than 10%, will secure for their owner the corresponding Annual Tonnage Tax reduction, as per Table 1.

Table 1: Attained EEXI, percentage of reduction Percentage of Reduction of Attained EEXI in relation to the Required EEXI Percentage of Annual Tonnage Tax reduction (%) Greater than 10 05 Greater than 15 10 Greater than 20 20 Greater than 30 25

To be eligible for this incentive, an owner must submit as attachment to the relevant application a copy of the International Energy Efficiency (IEE) Certificate with its Supplement.

2.2 Incentive 2: IMO Data Collection System (DCS)

The Environmental Incentive related to the Data Collection System (DCS) introduced by the International Maritime Organization (IMO), applies to ships of 5.000 GT and above, with at least 4.380 reported hours at sea per annum, which are subject to the provisions of Regulation 27 of the amended MARPOL Convention/ANNEX VI.

Ships that achieve a reduction of the total fuel consumption in relation to the total distance travelled between two consecutive reporting periods (yearx vs yearx-1) greater than 4%, will secure for their owner an Annual Tonnage Tax reduction (for yearx) as per Table 2:

| Table 2: Percentage of reduction of total fuel consumption / total distance travelled between two consecutive reporting periods |
| --- |
| Percentage of reduction between two consecutive reporting periods | Percentage of Annual Tonnage Tax reduction (%) |
| Greater than 4% | 10 |
| Greater than 6% | 15 |
| Greater than 8% | 20 |

To be eligible for this incentive, an owner must submit the following documents as attachments to the relevant application:

-	A copy of the Statement of Compliance-Fuel Oil Consumption Reporting, for two consecutive reporting periods; and

-	A copy of the Collected Data Summaries Report (MEPC.292 (71) / APPENDIX 2) for two consecutive reporting periods.

2.3 Incentive 3: Carbon Intensity Indicator (CII)

The Environmental Incentive related to the Carbon Intensity Indicator (CII) of the IMO applies to eligible ships of 5.000GT and above, which are subject to the provisions of Regulation 28 of the amended MARPOL Convention/ANNEX VI.

Ships that achieve an operational carbon intensity Rating A or Rating B in a year with at least 4.380 reported hours at sea per annum, will secure for their owner an Annual Tonnage Tax reduction for that year, as per Table 3:

| Table 3: Carbon Intensity Rating, percentage of reduction |
| --- |
| Carbon Intensity Rating | Percentage of Annual Tonnage Tax reduction (%) |
| Rating A | 20 |
| Rating B | 10 |

To be eligible for this incentive, an owner must submit attached to the relevant application copy of the Statement of Compliance–Fuel Oil Consumption Reporting and Operational Carbon Intensity.

3. Final Stipulations

The reduction for the aforementioned environmental incentives will be calculated cumulatively, and according to the relevant provisions of the Law the maximum percentage reduction-discount on the Tonnage Tax that a ship and its owner can receive is 30%.

An eligible ship for any of the above environmental incentives is a Cyprus ship or a Community ship that is within the Cyprus Tonnage Tax System and is engaged in maritime transport.

3.1 Additional provisions

- A ship that was detained for any environmental deficiency (ies) during a Port State Control inspection, during the calendar year for which its owner applies for an environmental incentive, is not eligible for any environmental incentive for the said year.

- A ship that violates any European Union legislation in force related to the environmental protection and relevant national harmonisation legislation (e.g Directive (EU) 2016/802 and the Specifications, Sustainability Criteria and Reduction of Fuel Emissions Law of 2022 (Law 106(I)/2022), Regulation (EU) 2015/757, Regulation (EU) No 1257/2013) during the calendar year for which its owner applies for an environmental incentive, is not eligible for any environmental incentive for the said year.

- A ship is eligible for any of the above mentioned environmental incentives, provided that the ship is not laid-up (warm or cold) at any time during the calendar year for which its owner applies for an environmental incentive.

______________

SDM March 2024 Final